## Slide 1: Real Time Scheduling
    Static Timer Driven Scheduling

## Slide 2: Static Timer Driven Cyclic Scheduling
When job parameters with hard deadlines are known in advance, a static schedule (containing all scheduling decision times) can be constructed offline.
Assume that the operating system maintains a queue for aperiodic jobs.
When an aperiodic job is released, it is placed in the queue without the attention of the scheduler.
assume jobs are ordered in a manner suitable for the applications in the system.
Whenever the processor is available for aperiodic jobs, the job at the head of this queue executes.

## Slide 3: Static Timer Driven Cyclic Scheduling
Whenever the parameters of jobs with hard deadlines are known before the system begins to execute, a straightforward way to ensure that they meet their deadlines is
To construct a static schedule of the jobs off-line, This schedule specifies exactly when each job executes.
According to the schedule, the amount of processor time allocated to every job is equal to its maximum execution time, and every job completes by its deadline.
During run time, the scheduler dispatches the jobs according to this schedule. Hence, as long as no job ever overruns all deadlines are surely met.

## Slide 4
  Scheduler will schedule periodic jobs using a static schedule that is computed offline and stored in a table T.
  Each entry (tk,T(tk)) gives a decision time tk, when scheduling decision is made and name of task T(tk).
  T(tk)= Ti if Ti is to be scheduled at time tk and
  I, if no periodic task is scheduled at time tk
  Example of Table Driven Schedule
Schedule Table
Task | Start time in ms
T1 | 0
T2 | 3
T3 | 10
T4 | 12
T5 | 17

## Slide 5
Eg:
There are four independent task
T1 = (4, 1), T2 = (5, 1.8), T3 = (20, 1), and T4 = (20, 2).
q1=0,p1=4,e1=1,D1=4
Their utilizations are
U1=e1/p1 = ¼ =.25
0.25, 0.36, 0.05, and 0.1, respectively, and the total utilization is 0.76.
Here length of hyperperiod is 20. According to static schedule amount of processor time allocated to array job is equal to maximum execution time and every job complete by its deadline.

## Slide 6
T1 = 0,4,8,12,16
T2= 2,7,12,17
T3=1,20
T4= 6,26

## Slide 8
T1 starts execution at time 0, 4, 9.8, 13.8, and so on; T2 starts execution at 2, 8, 12, 18, and so on. All tasks meet their deadlines.
Some intervals, such as (3.8, 4), (5, 6), and (10.8, 12), are not used by the periodic tasks. These intervals can be used to execute aperiodic jobs.

## Slide 9: Implementation:
It can be implemented by storing precomputed schedule as a table.
Tk = Indicate decision time when scheduling decision is made.
T(tk) = It will give name of task or I.
K | tk | T(tk)
1 | 0 | T1
2 | 1 | T3
3 | 2 | T2
4 | 3.8 | I
5 | 4 | T1
- | - | -
17 | 19.8 | I